## Slide 1: SD card bootloader for STM32
Tomas DRESLER

## Slide 2: Agenda
9:00 | About ST | Tomas POKORNY
 | Products Offer | 
9:10 | What is Bootloader? How to build one Practical demo & hands-on Impact on applications using bootloader | Tomas DRESLER
10:30 | End of session | 
Time
Speaker
Presentation

## Slide 3: Why to bother with a bootloader? /open question/

## Slide 4: How STM32 boots?

## Slide 5: STM32 (ARM Cortex-M) booting process
During Reset (after power-on or from other sources)
  Main oscillator starts, FLASH memory becomes ready
  Boot pins get sampled [BOOT0, (n)BOOT1], memory map is adapted
  Option bytes are loaded and applied
After Reset
  Vector table is expected at beginning of FLASH memory (the only link with program placement is the register NVIC->VTOR)
  Cortex-M reads top of MSP from address VTOR + 0x0000 0000
  Cortex-M reads Reset Handler address from address VTOR + 0x0000 0004 and jumps
  … to be continued on next slide

## Slide 6: STM32 (CMSIS & C RTL) booting process
CMSIS entry at Reset Handler
  Call to SystemInit (system_stm32f7xx.c) updates VTOR, initializes clock (and external memory interface, if needed)
  Call to C RTL entry (__main) or manual memory initialization
  Jump to main(void)
C RTL entry
  Initializes RW memory section (static and global variables with initialized values) by copy of init values from FLASH to RAM – several blocks, table describing the copy (or unpack) operations is created by linker
  Initializes ZI memory section by filling with zeros
  Initializes stack and heap internal pointers and zones
  Opens I/O channels (stderr, stdin, stdout), calls static class constructors, if C++ is used

## Slide 7: Program execution on a microcontroller
A C program starts in int main(void)
  Program isn’t expected to exit main, but safety net exists:
    atexit(fun), exit(), _Exit(), _kill() – can be overridden, see syscalls.c
  There is typically no operating system “above the application” to take control back
  At programmer’s shoulders is the implementation of safe handling of exceptions
    Watchdogs (SW, HW, safe external design – IEC 60 335, SIL)
    Issue logging and attribute collection for online identification
    User warning (dead device over ever-restarting device over user choice)
    System reset to prevent deadlock
    Preventing overheating, battery discharge

## Slide 8: How to update your application?

## Slide 9: In-Application Programming
Advantages
  An application can update itself, while in operation (let’s imagine a server power source)
  App can reuse any interface, even those with difficult protocols and huge SW stacks, with added encryption and security
Disadvantages
  Microcontroller needs double memory (for working and new version) – expensive
  If upgrade fails (power loss, ESD event), you can brick the application totally by damaging the vector table
  Needs dual bank architecture, which means more versions and relocatable code and data (difficult to maintain)

## Slide 10: Bootloader
Advantages
  Bootloader doesn’t change itself – safety: FLASH sector can be marked read-only
  It can be restarted easily in case of programming failure
  It is small, needs much less memory than IAP
Disadvantages
  Bootloader doesn’t change itself – release is kept forever, even in case of limitations
  It always occupies beginning of FLASH memory and time during boot
  Application needs to be adapted for an offset in memory placement

## Slide 11: External tools or services
Advantage
  Complete memory content upgrade possible
Disadvantages
  Transport of device or skilled technician needed
  Package disassembly
  External tools
  Unavailable if chip is locked down
  Expensive

## Slide 12: SD card bootloader implementation

## Slide 13: An SD card bootloader
Bootloader is a normal application
  Initializes clocks and peripherals (LCD, SD card, SDRAM, CPU)
  Opens FATFS file system on top of SD card drivers
  Opens files, reads them and processes the content
  Communicates with the user (LCD, buttons)
… but little different
  Erases FLASH memory outside of its own program scope
  Programs the FLASH memory, Option bytes
  Verifies the various application aspects (signature, version, CRC, entry points)
  Restores reset state of the MCU and jumps to the application entry point

## Slide 14: Bootloader program flow
RESET
Setup LCD
Setup SDRAM
Setup SDMMC
Mount FS
OK?
Setup CLK
1
Skip
1
2
Find *.def
OK?
Skip
Open *.def
OK?
Skip
Read all tokens
OK?
Skip
2
Close *.def
Version >= existing app
OK?
Skip
3
Open *.bin
OK?
Skip
3
Read into SDRAM
Close *.bin
OK?
Skip
4

## Slide 15: Bootloader program flow
4
5
Verify CRC
OK?
Skip
Verify signature
OK?
Skip
Verify version & length
OK?
Skip
5
Calculate sectors
Erase FLASH
OK?
Dead
6
Program FLASH
OK?
Dead
6
Verify FLASH
Reset clock & peripherals
OK?
Dead
7
Verify signature
OK?
Dead
7
Verify MSP & Reset
Jump to application
OK?
Dead
Skip

## Slide 16: Bootloader program flow
Other features to implement:
  Key to bypass version check: DONE
  Bootloader CRC check: DONE
  Signature written only after image has been fully programmed
  Length and CRC stored along for initial consistency check
  Replace CRC with SHA-1 and secret salt
  Option byte check and correction
Report to user
End
Dead
Freeze core (WFI)

## Slide 17: Bootloader implementation /Boot & FS/
HAL_Init();
/* Configure the system clock to 180 MHz */
SystemClock_Config();
/*##-1- Configure LCD ######################################################*/
LCD_Config();
LCD_LOG_SetHeader("SD bootloader version " VERSION);
LCD_LOG_SetFooter("Booting...");
/*##-2- Link the SD Card disk I/O driver ###################################*/
if (FATFS_LinkDriver(&SD_Driver, SD_Path) != 0)
SKIP_LOADER("Can't link SD driver");
/*##-3- Open filesystem */
if (f_mount(&fs, (TCHAR const*) "", 1) != FR_OK)
SKIP_LOADER("Can't open filesystem, is SD card inserted and formatted as FAT32?");
const Diskio_drvTypeDef SD_Driver =
{
SD_initialize,
SD_status,
SD_read,
SD_write,
#if _USE_IOCTL == 1
SD_ioctl,
#endif /* _USE_IOCTL == 1 */
};
DSTATUS SD_initialize(BYTE lun)
{
Stat = STA_NOINIT;
if(BSP_SD_Init() == MSD_OK)
{
Stat &= ~STA_NOINIT;
}
return Stat;
}

## Slide 18: Bootloader implementation /file ops/
/*##-4- Find description ###################################################*/
res = f_findfirst(&dir, &fno, "/", "app*.def");
while (fno.fname[0] && res == FR_OK) {
strcpy(originalFileName, fno.fname);
/* Search for last item */
res = f_findnext(&dir, &fno);
}
f_closedir(&dir);
/*##-5- Open description file ##############################################*/
if (f_open(&fle, originalFileName, FA_READ) != FR_OK)
SKIP_LOADER("Can't open description file %s", originalFileName);
if (f_read(&fle, &c, 1, &ln) != FR_OK || ln != 1) return -1;
f_close(&fle);

## Slide 19: Bootloader implementation /FLASH ops/
/* Unlock the Flash to enable the flash control register access *************/
HAL_FLASH_Unlock();
/* Allow Access to option bytes sector */
HAL_FLASH_OB_Unlock();
/* Get the Dual bank configuration status */
HAL_FLASHEx_OBGetConfig(&OBInit);
/* Turn on LED3 if FLASH is configured in Single Bank mode */
if ((OBInit.USERConfig & OB_NDBANK_SINGLE_BANK) == OB_NDBANK_DUAL_BANK)
SKIP_LOADER("Wrong FLASH DUAL_BANK option byte");
/* Erase FLASH sectors */
startSector = GetSector(APP_START);
endSector = GetSector(APP_START + imageSize);
/* Fill EraseInit structure*/
EraseInitStruct.TypeErase = FLASH_TYPEERASE_SECTORS;
EraseInitStruct.VoltageRange = FLASH_VOLTAGE_RANGE_3;
EraseInitStruct.Sector = startSector;
EraseInitStruct.NbSectors = endSector - startSector + 1;
if (HAL_FLASHEx_Erase(&EraseInitStruct, &endSector) != HAL_OK)
DEAD_END("FLASH erase failed at sector %d, stopping core. Reason: %d", endSector, HAL_FLASH_GetError());

## Slide 20: Bootloader implementation /FLASH ops/
FlashAddrW = APP_START;
uwImagePtrW = (uint32_t *)INTERNAL_BUFFER_START_ADDRESS;
fileSize = (imageSize + 3) & 0xFFFFFFFC; // round up for word access
while (fileSize) {
if (HAL_FLASH_Program(FLASH_TYPEPROGRAM_WORD, FlashAddrW, *uwImagePtrW) != HAL_OK)
DEAD_END("FLASH programming failed at address 0x%08X, stopping core. Reason: %d",
FlashAddrW, HAL_FLASH_GetError());
fileSize -= 4;
FlashAddrW += 4;
uwImagePtrW++;
}

## Slide 21: Bootloader implementation /CRC32/
CRC32 can be calculated for your binary here: https://emn178.github.io/online-tools/crc32_checksum.html
/* CRC setup */
__CRC_CLK_ENABLE();
hcrc.Instance = CRC;
hcrc.Init.DefaultPolynomialUse = DEFAULT_POLYNOMIAL_ENABLE;
hcrc.Init.DefaultInitValueUse = DEFAULT_INIT_VALUE_ENABLE;
hcrc.Init.InputDataInversionMode = CRC_INPUTDATA_INVERSION_BYTE;
hcrc.Init.OutputDataInversionMode = CRC_OUTPUTDATA_INVERSION_ENABLE;
hcrc.InputDataFormat = CRC_INPUTDATA_FORMAT_BYTES;
if (HAL_CRC_Init(&hcrc) != HAL_OK)
SKIP_LOADER("Can't setup CRC");
while(uwImagePtrW < &g_pfnVectors + (0xFFFC >> 2))
hcrc.Instance->DR = __REV(*uwImagePtrW++);
if(*uwImagePtrW != ~hcrc.Instance->DR)
DEAD_END("Bootloader corrupted, invalid CRC (0x%08X)", ~hcrc.Instance->DR);

## Slide 22: Bootloader implementation /The Jump/
/* here we go to verify image in memory */
uwImagePtrW = (uint32_t *)APP_START;
newMSP = *uwImagePtrW++;
if ((newMSP & 0xFF000000) != 0x20000000)
DEAD_END("Application has bad stack pointer, stopping core.");
jmpAddr = *uwImagePtrW;
if ((jmpAddr & 0xFF000000) != 0x08000000 && (jmpAddr & 0xFF000000) != 0x00000000)
DEAD_END("Application has bad entry point, stopping core.");
//-- reset peripherals to guarantee flawless start of user application
HAL_CRC_DeInit(&hcrc);
BSP_LCD_MspDeInit();
SysTick->CTRL &= ~SysTick_CTRL_ENABLE_Msk;
HAL_RCC_DeInit();
HAL_DeInit();
SCB_DisableDCache();
SCB_DisableICache();
/* let's do The Jump! */
__set_MSP(newMSP);
asm("bx %0\n" : : "r" (jmpAddr));

## Slide 23: Demo application

## Slide 24: A demo application
The application within bootloader environment needs little adaptation
  It shall be linked in memory BEHIND the bootloader, let’s say with 64 kB offset: FLASH start = 0x0801 0000
  The FLASH length in linker file shall be decreased by this offset: FLASH length = (512 – 64) kB
  The NVIC->VTOR needs to point to beginning of application vector table (remember to update system_stm32f7xx.c)
This is all!

## Slide 25: Thank you for your attention!